## Slide 1: Chapter 4
Design of polynomial-time
exact algorithm

## Slide 2: Outline
Review of complexity
A case study
  Optimal relay node assignment for cooperative communications

## Slide 3: Review of Complexity
Class P
  Exist a polynomial-time complexity algorithm
Class NP
  Exist a non-deterministic polynomial-time complexity algorithm
NP-hard
  Any problem in Class NP can be reduced to it in polynomial-time

## Slide 4: Review of Complexity (cont’d)
Unless P=NP, no polynomial-time algorithm to solve an NP-hard
or NP-complete problem
Existing a non-polynomial-time algorithm does not mean this
problem is not in P
NP-complete
  If it is in Class NP and is NP-hard
Notes: We will show an example in case study.

## Slide 5: Outline
Review of complexity
A case study
  Optimal relay node assignment (ORA) for cooperative communications

## Slide 6: Outline of Case Study
6
Cooperative communications (CC)
    Amplify and forward (AF)
    Decode and forward (DF)
Relay node assignment problem (RA)
ORA algorithm
Numerical results

## Slide 7: CC Network Model
Sender
Receiver
Relay Node
1st Time Slot
2nd Time Slot
1st Time Slot
7
Each node only has a single antenna
Transmission is done on a frame-by-frame basis
  One frame has two time slots
Notes: 1. CC is a recent advance in physical layer technology.
2. Two-slot structure is necessary due to half duplex nature of most wireless transceivers.
3. Antennas on sender and relay node cooperate to achieve spatial diversity

## Slide 8: Two Modes of CC
Amplify and forward
  1st time slot: Receives the signal
  2nd time slot: Amplifies and forwards the signal to destination node
Decode and forward
  1st time slot: Receives and decodes the signal
  2nd time slot: Forwards the decoded signal

## Slide 9: AF Mode – 1st Time Slot
The signal from s to d is
and the received signal at the relay node r is
1st Time Slot
1st Time Slot
Sender
Relay Node
Receiver

## Slide 10: AF Mode – 2nd Time Slot
The signal from r to d is
where
Sender
Relay Node
Receiver
2nd Time Slot

## Slide 11: AF Achievable Rate
Achievable rate is
where
and
Notes: By combining signals from s->d and s->r->d, the achievable rate is …

## Slide 12: DF Achievable Rate
Achievable data rate for DF is:
where
12

## Slide 13: Direct Transmission Achievable Rate
The achievable rate by direct transmission is
13
Achievable rate with CC may be higher or lower than direct transmission

## Slide 14: Outline of Case Study
14
Cooperative communication (CC)
  Amplify and Forward (AF)
  Decode and Forward (DF)
Relay node assignment problem (RA)
ORA algorithm
Numerical results

## Slide 15: A Cooperative Ad Hoc Network
s5
s4
s3
s2
s1
d1
d2
d3
d4
d5
r5
r4
r3
r2
r1
r6
r7
15
{ }: the set of source nodes;
  { }: the set of destination nodes;
  { }: the set of relay nodes.
  and

## Slide 16: Optimal Cooperative RNA Problem
A widely used performance metric: Achievable data rate
Aim to maximize the minimum achievable data rate among all source-destination pairs
    To ensure fairness
Relay node assignment affects achievable rate
  We need to determine optimal relay node assignment
16
Notes: Other performance metric can also be used

## Slide 17: Formulation for RNA
where
17
Integer variable
NP hard?
NP-hard formulation is not a proof of a problem’s NP-hardness
Notes: A source node si will be assigned at most one relay node
A relay node rj can be assigned to at most one source node

## Slide 18: Outline of Case Study
18
Cooperative communication
  Amplify and forward
  Decode and forward
Relay node assignment problem (RA)
ORA algorithm
Numerical results

## Slide 19: Basic Idea
Starting with any feasible relay node assignment
  Different initial relay node assignment can lead to the same optimal solution
  Special case: Use direct transmissions

## Slide 20: Basic Idea (cont’d)
Increasing objective Cmin during each iteration
  Identify the source node corresponding to Cmin (bottleneck node).
  Make adjustment to increase the achievable rate of this bottleneck node
    Make sure the new achievable rate is strictly greater than Cmin.
  If no adjustment is possible, the algorithm terminates

## Slide 21: ORA Procedure
Suppose s1 is the bottleneck node
Then s1 examines other relays with achievable rate larger than Cmin
  If no such relay, then ORA terminates.
  Otherwise, consider those relays in non-increasing order of achievable rates.
21

## Slide 22: ORA Procedure (cont’d)
Suppose r2 offers the largest achievable rate for s1
  If r2 is not assigned, then r2 can be assigned to s1 and current iteration is completed.
Otherwise, assume r2 is already assigned to s2. Mark s2 to indicate r2 is “under consideration” and check whether r2 can be released from s2.
22

## Slide 23: ORA Procedure (cont’d)
To release r2, s2 needs to find an unmarked relay node with achievable rate larger than Cmin
  If r3 is the only choice and is not assigned, then r3 can be assigned to s2 and r2 can be assigned to s1. Current iteration is completed.
  Otherwise, mark r3 and check whether r3 can be release by s3
23
Notes: or direct transmission

## Slide 24: ORA Procedure (cont’d)
If s3 cannot find any unmarked relay that offers a higher achievable rate than Cmin, then s2 cannot use r3 and s1 cannot use r2.
24
Notes: or direct transmission

## Slide 25: Clear Marks?
Now s1 needs to consider other relays. Do we need to clear marks on r2 and r3 here?
Naïve approach clears marks such that r2 and r3 can be re-considered
in this iteration
ORA does not clear marks
  Each relay node can only be
  considered once in one iteration
  Marks will be cleared at the
  end of the iteration

## Slide 26: ORA Procedure (cont’d)
s1 consider another relay r4
  If r4 is not assigned, it can be assigned to s1 immediately and current iteration is completed.
26

## Slide 27: ORA Procedure (cont’d)
  If r4 is assigned to other source, ORA continues.
27
s4 does not check marked nodes r2 and r3

## Slide 28: ORA Procedure (cont’d)
We have two outcomes for each iteration:
  If a better assignment is found, ORA identifies a new bottleneck node for the next iteration.
  If this iteration is non-improving, ORA terminates
28

## Slide 29: Example - Initial Relay Node Assignment
29

## Slide 30: Example - First Iteration of ORA Algorithm
30
Bottleneck node s3, Cmin=13
Notes: s3 checks r4, which is used by s2.
r4 cannot be released from s2, because all unmarked relay nodes cannot provide a higher achievable rate than Cmin
(2) s3 checks r7, which is used by s4.
r7 cannot be released from s4, because all unmarked relay nodes cannot provide an achievable rate larger than Cmin
(3) s3 checks r3, which is used by s5
s5 can use unmarked relay r2 and has an achievable rate larger than Cmin. Thus, r3 can be released from s5. Therefore, r2 is assigned to s5 and r3 is assigned to s3
30

## Slide 31: Example - Second Iteration of ORA algorithm
31
Bottleneck node s1, Cmin=15
Notes: (1) s1 checks r2, which is used by s5.
(a) s5 checks r4, which is used by s2
r4 cannot be released from s2, because all unmarked relay nodes cannot provide an achievable rate larger than Cmin
(b) s5 checks r7, which is used by s4
r7 cannot be released from r4, because all unmarked relay nodes cannot provide an achievable rate larger than Cmin
(c) s5 checks r3, which is used by s3
r3 cannot be released from s3, because all unmarking relay nodes cannot provide an achievable rate larger than Cmin
Thus, s2 cannot be released from s5
(2) s1 checks r6, which is used by s6.
Then, s6 checks r1 and finds r1 is available because r1 is unmarked and can provide an achievable rate larger than Cmin. Thus, r6 can be released from s6. Therefore, s1 uses r6 and s6 uses r1
31

## Slide 32: Example - Third Iteration of ORA Algorithm
32
Bottleneck node s7, Cmin=16
Notes: s7 check r5, which is not assigned and can provide an achievable rate larger than Cmin
so r5 can be assigned to s7 immediately.
32

## Slide 33: Example - Last Iteration of ORA Algorithm
33
Bottleneck node s3, Cmin=17
Notes: s1 and s3 have the same Cmin. A tie is broken by taking the node with the largest node index.
s3 checks r4, which is used by s2
r4 cannot be released from s2, because all unmarked relay nodes cannot provide an achievable rate larger than Cmin
(2) s3 checks r7, which is used by s4
r7 cannot be released from s4, because all unmarked relay nodes cannot provide an achievable rate larger than Cmin
(3) s3 does not have other choice. ORA is complete.
33

## Slide 34
Complexity Analysis
  Before first iteration
    Step 1:
    Step 2:
    Step 3:
  Each iteration
    A source node needs to check at most relay nodes
    The number of source nodes is
    The complexity of an iteration is
  Number of iterations
    The number of iteration is
Overall complexity is:
Notes: Refer to Figure 4.6: A pseudocode for the ORA algorithm
The dominant component in complexity is the recursive process of searching an unmarked relay node and checking its availability.
This process may involve all source nodes, each of which checking its relay nodes’ marking status and availability.

## Slide 35: Naïve Approach
35
Perform both marking and unmarking within an iteration.
It considers all possible assignments
  Guarantee optimal solution
The complexity is exponential
  , if
  , if
Notes:   The complexity analysis will be a homework problem.
35

## Slide 36: ORA v.s. Naïve Approach
Naïve approach
  Guarantee to find optimal solution
  Exponential time
ORA algorithm
  Polynomial time
  Optimal?
We will prove that ORA can guarantee optimality
36

## Slide 37: Proof of Optimality - Notation
37
The proof is based on contradiction

## Slide 38: Proof of Optimality - Key Idea
38
We will prove
  Fact 4.1: is not marked at the end of the last ORA iteration
  If exists, then we will show that is marked at the end of the last ORA iteration
It contradicts with Fact 4.1, so a better solution does not exist.
Notes: In ORA algorithm, a relay node rj is marked only if rj is not the relay node assigned to sb.
Then we have Fact 4.1.

## Slide 39: Proof of Optimality - Claim 4.1
Claim 4.1: Relay node must be marked at the end of the last ORA iteration. Further, it cannot be and must be assigned to some source node under .
Proof:
  Prove that must be marked:
    is a better solution, so

## Slide 40: Claim 4.1(cont’d)
    ORA should have checked the relay node ’s available and find it is unavailable
    Thus, must be marked and will not be cleared in the last iteration.
  Prove that cannot be :
    If it is , sb will choose direct transmission in the last iteration, since
    This contradicts that the last iteration is non-improving.
  Since is marked, it must be assigned to some relay node.
40

## Slide 41: Proof of Optimality
By the definition of , we have that is assigned to source node in .
Define as .
41

## Slide 42
Claim 4.2: Relay node must be marked at the end of the last ORA iteration. Further, it cannot be and must be assigned to some source node under .
  The proof follows the same token as that for Claim 4.1
Proof of Optimality - Claim 4.2

## Slide 43: Proof of Optimality
Define
We have two cases:
  If source node is a node in , we terminate our recursive procedure
  Otherwise, we can further consider in
We use following general notations
  and

## Slide 44: Proof of Optimality
Since the number of source nodes are finite, our recursive procedure will terminate in finite steps. Suppose we terminate at k=n.

## Slide 45: Proof of Optimality - Claim 4.3
Claim 4.3: Relay node must be marked at the end of the last ORA iteration. Further, it cannot be and must be assigned to some source node under solution , k=0, 1, 2, …, n.
45

## Slide 46: Proof of Optimality - Claim 4.3
Proof:
  Prove that must be marked:
    is a better solution, so
    ORA must have checked ’s availability for
    and find it is unavailable.
    Thus, must be marked at the last iteration.
  Prove that cannot be :
    If it is , will choose in the last iteration, since it can offer
46

## Slide 47: Claim 4.3(cont’d)
    sb will be able to get a better relay node. This contradicts with fact last iteration is non-improving.
  Since is marked, it must be assigned to some source node
47

## Slide 48: Proof of Theorem 4.1
Theorem 4.1. Upon the termination of ORA algorithm, the obtained solution is optimal.
Proof:
  Under Claim 4.3, we prove relay node is assigned to a source node in .
  Current iteration procedure terminates at , . Its assigned source node in must be in
48

## Slide 49
Proof of Theorem 4.1 (cont’d)
But in , source nodes have their relay nodes , respectively
Then can only be assigned to sb under
is assigned to sb under
So

## Slide 50: Proof of Theorem 4.1 (cont’d)
Claim 4.3 states that must be marked at the last iteration. But Fact 1 says is not marked.
We reach contradiction, the proof is complete
Thus, does not exit, and is optimal
50

## Slide 51: Outline of Case Study
51
Cooperative communication
  Amplify and forward
  Decode and forward
Relay node assignment problem
ORA algorithm
Numerical results

## Slide 52: 100-node Network Topology: Case 1 (Nr>Ns)
Ns =30 and Nr =40
52

## Slide 53: Case 1: Result
53
Notes: Different initial assignment can lead to an optimal solution.
ORA algorithm can always lead to a better solution than direct transmission.

## Slide 54: Case 1: Optimal Assignment
142% improvement
54

## Slide 55: 100-node Network Topology: Case 2 (Nr<Ns)
Ns=40 and Nr=20
55

## Slide 56: Case 2: Result
56
Notes: Different initial assignment can lead to an optimal solution
ORA algorithm can always lead to better solution than direct transmission.

## Slide 57: Case 2: Optimal Assignment
108% improvement
57

## Slide 58: Summary
Review of complexity
Case study
  Optimal relay node assignment for cooperative communications
  Developed a polynomial time algorithm (ORA) to solve the problem.
    Key idea: linear marking mechanism
  Offered a proof for optimality
  Numerical results showed significant improvement in network achievable rate.
58