## Slide 1: Chapter 10
An Effective Technique for Mixed-integer Optimization

## Slide 2: Outline
Sequential fixing: An introduction
Case study
  Spectrum sharing in cognitive radio networks

## Slide 3: Basic Idea
Since a MINLP problem is NP-hard in general, we aim to obtain a near-optimal solution
Branch-and-bound framework can guarantee (1-e)-optimal solution to MINLP, but its worst case complexity is exponential
A heuristic algorithm: Sequential fixing
  Competitive solution for certain MINLP and any MILP
    Problem is reduced to LP once we know the values of all integer variables
  Iteratively determine integer variables
  Determine other variables via LP
3

## Slide 4: Determine all Integer Variables
The performance of the solution depends on the values of integer variables
  If we can obtain the optimal values of integer variables, the obtained solution is optimal
Key challenge: How to determine the integer variables?
Approach:
  Solve the linear relaxation of the problem
  Fix one or more integer variables based on the solution to the LP-relaxed problem
  Repeat the above steps until all integer variables are fixed
4
Notes:   “Solve the linear relaxation of the original problem”: (1) integer variables  continuous variables; (2) eliminate nonlinear terms (by reformulation).
  “the remaining variables can be obtained by solving an LP”: This is true only when the nonlinear terms can be removed by some techniques. That’s why not all MINLP can be solved by SF.

## Slide 5: SF Framework
Relax all integer variables and solve the relaxed LP
Fix the variable whose value is closest to integer
If some integer variables are unfixed, reformulate and solve a newly relaxed LP with the newly fixed variables, go step 2
Otherwise, formulate and solve the LP based on all fixed variables. Done!
5
Polynomial time complexity!
step 2
Notes: An example of step 2: Suppose xi = {0, 1, 2, 3}. From relaxed LP, we obtained: x1=1.5, x2=2.8, x3=1.9, x4=0.4. We fix x3 to 2.
Further, we may fix multiple variables in one iteration, e.g., fix x3 to 2 and x2 to 3.

## Slide 6: Performance Analysis (for a minimization problem)
Develop a lower bound
Compare the obtained solution with the lower bound
If the obtained solution is close to the lower bound, then
  The lower bound is tight
  The obtained solution is even closer to the optimum
6
Notes: Note: if the original problem is a maximization problem, we should develop an upper bound as a performance reference

## Slide 7: Outline
7
Sequential fixing: An introduction
Case study
  Spectrum sharing in cognitive radio networks
Notes: 7

## Slide 8: Dynamic Spectrum Access
Spectrum is densely allocated to a variety of systems
Many allocated spectrum blocks are not used in certain geographical areas and are idle most of the time
Dynamic Spectrum Access (DSA) can be employed to improve spectrum usage
  Wireless devices are allowed to sense and explore a wide range of frequency spectrum for data communication
8

## Slide 9: Cognitive Radio
Each node can sense available spectrum
  Each node may have a different set of available spectrum (or channels)
  Each frequency band is likely to have different bandwidth
Each node can transmit over non-contiguous frequency bands
  Radio may switch frequency bands on a per-packet basis
9

## Slide 10: Cognitive Radio Networks
A set of user sessions with certain data rate requirements
Multi-hop routing
Dynamic spectrum access
10
Cognitive Radio Network

## Slide 11: Outline of Case Study
11
Problem statement and formulation
Find a lower bound
A near-optimal solution based on SF
Numerical Examples
Notes: 11

## Slide 12: Problem Statement
Problem Setting:
  Multi-hop cognitive radio network
  Available frequency bands at each node may be different; each frequency band may be of different size
  A set of communication sessions, each with a data rate requirement
Objective: Minimize the total used spectrum resource
Question: How to perform spectrum allocation, scheduling, and routing?
12

## Slide 13: Spectrum Sharing and Sub-band Division
There is a set of M un-equal bands in the network
Each node has a subset of bands available
For scheduling, we further divide a band m into K(m) sub-bands
13
Notes: W(m) is the bandwidth of band m

## Slide 14: Transmission Range and Interference Range
Follow protocol interference model
  Transmission range
where b is an antenna related constant, r is transmission power spectral density at a transmitter, rT is transmission power spectral density to decode a transmission at a receiver, and n is the path loss index.
  Interference range
Denote
14
where rI is the max threshold of power spectral density for interference to be negligible at a receiver

## Slide 15: Scheduling and Interference Constraints
A node i cannot transmit to multiple nodes on the same sub-band
A receiving node j cannot be in the interference range of any other transmitting nodes on the same sub-band
15

## Slide 16: Flow Routing
For each session, allow flow splitting for maximum flexibility (and optimality)
Flow balance constraints for session l:
  If node i is the source node, then
  If node i is the destination node, then
  For all other nodes, we have
16
redundancy
Notes: (1) fij(l) denotes data rate that is attributed to session l on link (i, j)
(2) r(l) denotes the rate of session l
(3) s(l) denotes the source node of session l
(4) d(l) denotes the destination node of session l
(5) “redundancy” means that the second constraint will be satisfied automatically as long as the first and the third constraints are satisfied

## Slide 17: Link Capacity Constraint
Capacity on link ij on sub-band (m,k)
Aggregate flow on link ij cannot exceed link capacity
17
Notes: (1) gij denotes propagation gain from node i to node j, ρ denotes transmission power spectral density at a transmitter, η denotes ambient Gaussian noise density.
(2) L denotes the set of active user sessions in the network.

## Slide 18: Problem Formulation
18
A mixed-integer non-linear program (MINLP)
non-linear
integer
Band division
constraint
Transmission
constraint
Interference
constraint
Link capacity
constraint
Flow balance
constraint

## Slide 19: Outline of Case Study
19
Problem formulation
Find a lower bound
A near optimal solution based on SF
Numerical Examples
Notes: 19

## Slide 20: Linear Relaxation
A lower bound can be found via linear relaxation to the MINLP problem
  Relax integer variables: integer  continuous
  Remove nonlinear terms: let
20

## Slide 21: Relaxed LP
21
constant
continuous
This problem can be solved in polynomial time.

## Slide 22: Outline of Case Study
22
Problem formulation
Find a lower bound
A near-optimal solution based on SF
Numerical Examples
Notes: 22

## Slide 23: Main Idea
Determine all x-variables iteratively via a series of LPs
  If in the relaxed problem formulation is close to 1, then sub-band (m, k) may be used for transmission on link ij
  Therefore, set
At each iteration, one or more x-variables can be fixed
Once all x-variables are fixed, the routing problem can be solved via a single LP
23

## Slide 24
Set up a LP problem by relaxing its binary variables to , and solve it
Fix the largest x-variable to 1
If some x-variables are unfixed, reformulate and solve a newly relaxed LP with the newly fixed x-variables, go step 2
Otherwise, formulate and solve the LP based on all fixed x-values. Done!
24
Algorithm Details
step 2
Notes: Step 2: The reason why we set the largest x-variable to 1 rather than set the smallest x-variable to 0 is that more x-variables may also be determined based on relevant scheduling and interference constraints.
Step 3: During the reformulation, if an x-variable is fixed to 1, its corresponding s variable (=x u) can be replaced by u; otherwise, s can be replaced by 0.

## Slide 25: An Iteration-Speedup Technique
To further decrease the complexity, we can fix more x-variables during each iteration
  Choose a threshold a, and fix all x-variables greater than a to 1
Justification of this approach
  Fixing multiple x-variables to 1 means that multiple links can be active simultaneously
  From the space perspective, two links far from each other will not interfere each other
  From the frequency perspective, no interference exists between two links if they use different sub-bands
25
Notes: Impact of the threshold value:
The solution complexity increases as threshold value increase
The solution performance may improve as threshold value increase

## Slide 26: Outline of Case Study
26
Problem Formulation
Find A Lower Bound
A Near Optimal Solution Based on SF
Numerical Examples
Notes: 26

## Slide 27: Simulation Setting
20, 30, and 40 nodes in a 500x500 area
5 active sessions with a rate in [10, 100] Mbps
Each band can be further divided for scheduling
Transmission range is 100m; interference range is 150m
Other parameters
27
Notes: All units normalized
Transmission range 20; interference range 30

## Slide 28: Results for 20-node Network
Normalized Results: Results from SF algorithm / a lower bound
Average 1.04
Standard derivation: 0.07
The solution from SF, the optimal solution, and the lower bound are the same!
 The solution obtained by SF is optimal
28
The solution is close to the lower bound
The solution is even closer to the optimum
The lower bound is very tight
The simulation results demonstrate:
Notes: Normalized Cost (w.r.t. Lower bound): the ratio of the objective value of the obtained solution by SF to its lower bound.

## Slide 29
Results for The First 40 Data Sets
29
Notes: (1) We can see that the solution is close to the lower bound. That is, the solution is even closer to the optimum.
(2) Only 40 data sets are presented because of the limited space. The remaining data sets can draw the same conclusions.

## Slide 30
Normalized results:
Average 1.10
Standard derivation 0.16
Results for 30&40-node Network
30-node network
40-node network
Normalized results:
Average 1.18
Standard derivation 0.16
30
Notes: The simulation results illustrate that both of average value and standard derivation are small. This indicates that the obtained solution by SF is near optimal.

## Slide 31: Summary
Introduced the SF technique for mixed integer optimization
Investigated spectrum allocation, scheduling, and routing problem for CRN
Formulated a cross-layer optimization problem
Developed a near-optimal algorithm via SF technique
  Near optimality was substantiated by comparing a lower bound
  The complexity of the algorithm is polynomial time
31