## Slide 1: Chapter 8
Approximation algorithm and its applications
Part 1

## Slide 2: Review of Approximation Algorithm
Constant-factor approximation algorithm
  Maximization problem: Obtained feasible solution is
  at least cOPT
  Minimization problem: Obtained feasible solution is
  at most cOPT
(1-ε)-optimal (or (1+ε)-optimal) approximation algorithm
  Maximization problem: Obtained feasible solution is
  at least (1-ε)OPT
  Minimization problem: Obtained feasible solution is
  at most (1-ε)OPT
Notes: Constant-factor approximation algorithm: OPT >0 (unknown) is the optimal objective value, c<1 and is a constant for a maximization problem (c>1 and is a constant for a minimization problem)
The complexity is polynomial time.
(1-epsilon)-optimal (or (1+epsilon)-optimal) approximation algorithm: OPT >0 (unknown) is the optimal objective value, 0<epsilon <<1 and epsilon can be arbitrarily small
The complexity is polynomial function of 1/epsilon

## Slide 3
Base Station Placement Problem
Case Study

## Slide 4
Network Setting
Sensor nodes
  Transmit data to the base station via multi-hop
  Have limited energy
Network lifetime
  Many definitions
    In this case study, network lifetime is defined as the time until any node uses up its energy

## Slide 5: Base Station Placement (BSP) Problem
Motivation
  Fact: Base station location has a profound impact on network lifetime
Objective
  Determine the optimal base station location so as to maximize network lifetime
  Also optimize routing

## Slide 6
Energy Consumption Modeling
Communication power is the dominant part of energy consumption
Transmission power modeling
where
Receiving power modeling
Notes: fij is data rate that node i transmits to node j.
Cij is the cost associated with link i -> j.
beta_1 and beta_2 are constant coefficients
Alpha is path loss index
dij is the physical distance between sensor node i and j
Rho is a constant coefficient

## Slide 7
Impact of Base Station Location
Base station location has profound impact on energy consumption and network lifetime
We can determine the
maximum network lifetime
achieved on a location
Where to place base station
Notes: From the energy consumption model, we can see that flow rate and distance influence energy consumption
The maximum network lifetime achieved on a location can be solved by a linear program (see next slide).

## Slide 8
For A Given Base Station Location
Where and are constant.
Linear Programming
We can determine maximum network lifetime in polynomial-time

## Slide 9
Naïve Approach
Determine the network lifetime for each possible location
Compare these network lifetimes and choose the maximum
Infinite search space !!!
Notes: We can solve LP for each given location.
Search space is the set of all possible base station locations
However, this is unrealistic because the search space is infinite.

## Slide 10
Formulation for BSP
  where is the base station location and
  is an area of base station location
Non-convex function
Non-convex Programming !!!
Notes: First constraint is flow balance.
Second constraint is energy consumption, which joint consideration of base station location and multi-hop routing.
Third constraint is from transmission power modeling.
Non-convex programming is NP-hard in general.

## Slide 11
Basic Idea of Our Approach
Sub-area division
  With tight bounds on transmission cost for any point in the subarea
Fictitious cost point (FCP) presentation
  Change infinite search space into finite search space
The best FCP provides (1-ε)-optimal solution

## Slide 12
Smallest Enclosing Disk (SED)
To maximize network lifetime, the base station must be within SED
  Smallest disk that covers all sensor nodes
  Can be found in polynomial-time

## Slide 13
Based on contradiction
  Assume the optima base
  station location p is
  outside SED.
  For each sensor node ,
  we have diq<dip.
  Consequently, Ciq<Cip.
  We can save energy on every sensor node by relocating p to q. The network lifetime will be increased.
  Thus, p cannot be optimal.
Proof
Notes: Let q be the intersecting point between the line segment [p, OA] and the circle of SED

## Slide 14
Sub-area Division
Divide SED by a sequence of circles with radius D[h] and center node
Notes: The left SED is divided by a sequence of circles with center node 4.
The right SED is divided by sequence of circles at all nodes. This SED is divided into 28 irregular subareas.
D[h] will depend on next slide.

## Slide 15
Determine
Denote , where is the maximum distances between sensor node and the base station B.
Denote and the minimum and maximum costs between sensor node and base station B. We have and
Define , h=0,1,2, …,
For each C[h], compute the corresponding distance D[h]

## Slide 16
Property of A Sub-area
A subarea must be enclosed within some arc centered at sensor node
  Denote the index of this arc as
  For subarea (q1, q2, q3) and sensor node 3, its h3() is 2
For any point p in a sub-area and a sensor node , the transmission cost ciB(p) can be tightly bounded
  and
  For subarea (q1, q2, q3) and sensor
node 3, we have
and
Notes: Arc(q1,q2) represents the arc between q1 and q2

## Slide 17
Fictitious Cost Point (FCP)
Denote the FCP for subarea (m=1,2,…,M) as pm
It is represented by an N-tuple vector
  The -th element being upper bound of cost for any point in subarea to the -th sensor node
  The N-tuple cost vector for FCP pm is
with

## Slide 18
Property of FCP
For any point and the corresponding FCP pm, we have
Proof:
  From the definition of FCP pm, we have
Notes: The first equality is hold by definition of FCP
The second equality is hold by property of subarea
The inequality is hold by property of subarea

## Slide 19
Locate the Base Station
  Solve an LP for each FCP to find maximum network lifetime
Find the best FCP with the largest network lifetime
Place the base station at any point in the corresponding sub-area

## Slide 20
Summary:
A -optimal Approximation Algorithm

## Slide 21
An Example – Network Setting
We set α=2, β1=1, β2=0.5, and ρ=1
For illustration, we set the error bound to ε=0.2
Notes: We use a small 3-node network to illustrate the steps of the approximation algorithm.
The location, data rate, and initial energy for each sensor are shown in following table, where the units of distance, rate, and energy are all normalized.

## Slide 22
An Example – Algorithm Details
(1) We identify SED with origin = 0.61, 0.57 and radius =0.51
(2) We first have for each node . We then find the lower and upper bounds of ciB for each node , as follows

## Slide 23
An Example – Algorithm Details (cont’d)
(3) For each node , we find
and

## Slide 24
An Example – Algorithm Details (cont’d)
(4) We draw circles centered at
each node and with cost C[h],
1≤h≤Hi=3, to divide the whole
disk into 16 subareas
(5) We define a FCP pm for each
subarea , 1≤m≤16
  For example, for FCP p1, we define a 3-tuple cost vector as =

## Slide 25
An Example – Algorithm Details (cont’d)
(6) We apply LP on these 16 FCPs and obtain the network lifetime for each FCP
(7) Since the FCP p9 has the maximum achievable network lifetime 226.47 among all 16 FCPs, we can place the base station at any point in subarea ,
e.g., pε=(0.6, 0.6)
(8) We apply LP on pε and obtain (1-ε)-optimal network lifetime Tε=227.07. This completes the algorithm.

## Slide 26
Roadmap for Proof
Denote Topt the maximum network lifetime under optimal base station placement popt
Denote T* the maximum network lifetime under the best FCP p*
Denote Tε the network lifetime under a physical point pε in the subarea corresponding to the best FCP p*
We first prove that T* for the best FCP is with (1-ε) of the optimum, i.e., T*≥(1-ε)Topt
Then we show that for the physical point pε, its corresponding network lifetime is Tε no less than T* and thus also (1-ε) of the optimum, i.e., Tε≥T*≥(1-ε)Topt

## Slide 27
Correctness Proof
For T*and Topt as defined, we have T*≥(1-ε)Topt
To prove this, we first prove the following result, which is a general case
For any given base station location p, corresponding optimal routing solution φ, and achievable network lifetime T, denote the subarea that contains p for a given ε. Then for the corresponding FCP pm, its achievable network lifetime Tm is at least (1-ε) of T,
i.e., Tm≥(1-ε)T.

## Slide 28
Correctness Proof (cont’d)
Proof:
  We use the same routing φ on pm. Denote the network lifetime for FCP pm under φ, we have .
  Then we only need to show .
  We compute the total consumed energy on node
  under φ at time (1-ε)T. We find that the consumed energy is no more than its initial energy
  Thus, the network lifetime under routing solution φ is at least (1-ε)T.
  As a result, We have . This completes the proof.
Notes: Please see book chapter Lemma 8.2 for details.

## Slide 29
Correctness Proof (cont’d)
For Tε and Topt as defined, we have Tε≥(1-ε)Topt.
Proof:
  Denote the network lifetime for point pε under the same routing solution φ* for FCP p*. Since φ* is a sub-optimal routing for pε, we have . We already proved
  Thus, to show Tε≥(1-ε)Topt, we only need to show
  We compute the total consumed energy on node
  under φ* for point pε at time T*. We find that the consumed energy is no more than its initial energy
  Thus, the network lifetime for location pε under φ* is at least T*. As a result, the maximum network lifetime Tε for location pε is at least . This completes the proof.
Notes: Now we prove next result

## Slide 30
Complexity Analysis
The complexity is measured by the number of LPs, which equal to the total number of subareas
The maximum number of subareas is upper bounded by
  is total number of circles
Then

## Slide 31
Numerical Results
10-node network
20-node network
Tε=359.17 by (0.59, 0.31)
Tε=82.91 by (0.31, 0.79)
Notes: For 10-node network, we find that FCP with cost vector [1.05, 1.28, 1.05, 1.22, 1.16, 1.05, 1.05, 1.05, 1.41, 1.05] has maximum network lifetime T*=357.49, which is at least 95% of the optimal. By placing base station in the correspond subarea, e.g., at point (0.59,0.31), the network lifetime is 359.17>T*.
For 20-node network, we find that FCP with cost vector [1.55, 1.05, 1.16, 1.05, 1.41, 1.22, 1.41, 1.22, 1.41, 1.28, 1.63, 1.05, 1.16, 1.98, 1.71, 1.16, 1.28, 1.80, 1.05, 1.05] has maximum network lifetime T*=82.86 among all FCPs. We place base station in the correspond subarea, e.g., at point (0.31, 0.79). The network lifetime is 82.91>T*, which is also at least 95% of the optimum.

## Slide 32
Numerical Results
50-node network
100-node network
Tε=135.17 by (0.51, 0.68)
Tε=61.73 by (0.57, 0.52)

## Slide 33
Summary
Review of approximation algorithms
  Constant-factor approximation algorithm
  (1-ε)-optimal (or (1+ε)-optimal) approximation algorithm
Base station placement problem
  Change infinite search space into finite search space
  Represent each sub-area by a FCP
  The best FCP provides a (1-ε)-optimal solution